Air Pollution at Incinerator and Health Risk Assessment

# Abstract

This study aimed to assess the health risk associated with the inhalation of air pollutants including VOCs and heavy metals for workers at waste incinerator site in the South of Thailand. Air samples were collected and analyzed followed by NIOSH standard method, air samples were collected for 8 hours continuously. The concentration of heavy metal; Hg, Cd, Pb, Mn, Ni were very low while mean concentrations of VOCs; benzene, toluene, ethylbenzene, xylenes, and styrene were determined as 0.080, <0.001, 0.031,	0.043, and <0.001 mg/m3 respectively. Health risk assessment was employed to evaluate the carcinogenic and non-carcinogenic effects. The cancer risk for benzene exposure was estimated to be 1.26 x 10-5 that is higher than the acceptable risk level of 
1 x 10-6. Non-carcinogenic risk (Hazard Quotients; HQ) for toluene, ethylbenzene, xylenes and styrene were was at acceptable level. Thus, workers in this plant were at risk to health effects associated with benzene via inhalation exposure. Health promotion  and risk communication should be given to them in appropriated way.

Keywords : Waste Incinerator,  Health Risk Assessment, Occupational Health, Air pollution

# 1. Introduction

Waste incinerator is one of solid waste management technology which has been gearing up in Thailand [1]. However, incomplete combustion is a cause of organic compound emission such as aldehydes, chlorinated hydrocarbons, PAHs, polychlorinated dibenzodioxins, dibenzofurans et.al., which leading to environment and health effects [2]. The previous studies have found that living within 3 kilometers from an incinerator plant have an increased risk of lymphoma and soft tissue sarcoma cancer up to 3.5% . More evidence shown people living close to an incinerator has related to respiratory disease [3-4]. In particular the incinerator related workers were exposed to particulate and heavy metal 10 to 100 folds greater than that of general population  [5]. This study aimed to assess the health risk for the solid waste incinerator related workers.

# 2. Materials and Method

2.1 Study Area and Study Population

This study selected waste-to-energy plant in the Southern part of Thailand. Thirty incinerator related staff and workers were randomly selected under the condition of three different working environments which are including fuel feeding area, operation office, and administrative office.

2.2 Personal information: Questionnaires were used to collect information for exposure assessment which are general information (gender, age, weight, height) and operating information (jobs description, working hour, working frequency and working period.

2.3 Air sampling and analysis procedure

Air pollution exposure study was conducted by environmental sampling and hygiene survey during March – April 2015 as following,

(1) Workplace air sampling: air samples were collected 8 hours-working continuously by personal pump at each working environments. Sampling, preserving and analyzing were follow NIOSH standard method.

(2) Personal information : questionnaires were used to obtain information for exposure assessment which are general information (gender, age, weight, height) and operating information (responsibility, working hour, working frequency, working period)

This study was approved by the Ethics Review Committee for Research, Department of Health, Ministry of Public Health.

2.4 Health Risk Assessment

In this study, inhalation risk assessment were conducted following the  Risk Assessment Guidance for Superfund [6] as following equations.

EC	 = 	(CA x ET x EF x ED) / AT

Cancer risk for benzene (leukemia) and ethylbenzene (liver hepatocellular adenoma or carcinoma) was calculated following

Cancer risk 		=	IUR x EC

Non-carcinogenic risk for benzene, toluene, ethylbenzene, xylene and styrene was calculated following

Hazard Quotient	= 	EC / RfC

Where

| EC | is exposure concentrations (mg/m3) |  |
| --- | --- | --- |
| CA | is contaminants concentration in air (mg/m3) | Air monitoring during 8 hours |
| ET | is exposure time (hours/day) | 8 hours/day (8 hours day-shift) |
| EF | is exposure frequency (days/year) | 312 days/year |
| ED | is exposure duration (years) | 5 years |
| AT | is averaging time - When estimating cancer risk, AT calculated by lifetime (70 years) x 365 days/year x 24 hours/day - When calculating HQ for non-cancer effect, AT calculated by ED (5 years) x 356 days/year x 24 hours/day |
| IUR | is inhalation unit risk - IUR for Benzene (Leukemia) is 7.8 x 10-6 per µg/m3 [7] |
| RfC | is inhalation reference concentration - RfC for Benzene (decreased lymphocyte count) is 3 x10-2 mg/m3 [7] - RfC for Ethylbenzene (developmenta toxicity) is 1 mg/m3 [8] - RfC for Toluene (neurological effects) is 5 mg/m3 [9] - RfC for Xylene (impaired motor coordination) is 1 x10-1 mg/m3 [10] - RfC for Styrene (CNS effect) is 1 mg/m3 [11] |
| Cancer risk | Cancer risk of more than 10-6 considers an unacceptable level for carcinogenic effect of concern. |
| HQ | HQ and HI of more than 1 consider an unacceptable level for non-carcinogenic effects. |
| HI | Hazard Index (multiple substances) |

# 3. Results and discussion

3.1 General characteristic

Waste management technology is a stoker incineration with reverse-acting grate. The overall availability is 600 tons/day and generates electricity up to 14 MW for using in plant 24 hours continuously and sale for Provincial Electricity Authority. The pollution control systems are Semi Dry Scrubber, Bag Filter, and CEMs.

Sample population is 30 incinerator’s staffs included 18 men (60%) and 12 women (40%).  There are 6 feeding staffs (20%), 9 operation staffs (30%), and 15 office staffs (50%). The average age is 32.17 (±8.26) years.

3.2 Concentration of air pollution at the waste incinerator site

The 8 hours average all heavy metal and VOCs concentrations in differences sampling  areas are presented in Table 1. The concentration of mercury was under the detection limit, while concentrations of cadmium, lead, manganese, and nickel were less than 0.001 mg/m3, there were not included in the calculation of cancer risk and non-cancer risk (HQ). However, mean concentrations of benzene, toluene, ethylbenzene, xylenes and styrene were 0.080, <0.001, 0.031, 0.043, and <0.001 mg/m3 respectively. The concentration of each chemical was derived from sampling  area, concentrations of  benzene,  ethylbenzene and  xylenes in operation room and office  is higher than feeding area. Ventilation may be related to the result because the operation office and the administrative office are closed system while the feeding area is open system.

Table 1 Concentration of air pollution at the waste incinerator site.

| Sampling Area | Concentration (mg/m3) |
| --- | --- |
|  | Air Heavy Metal | Air VOCs |
|  | Hg | Cd | Pb | Mn | Ni | Benzene | Toluene | Ethylbenzene | Xylene | Styrene |
| Feeding Area | ND | <0.001 | <0.001 | <0.001 | <0.001 | 0.056 | <0.001 | 0.0005 | 0.0005 | <0.001 |
| Operation Room | ND | <0.001 | <0.001 | <0.001 | <0.001 | 0.097 | <0.001 | 0.0417 | 0.0412 | <0.001 |
| Office | ND | <0.001 | <0.001 | <0.001 | <0.001 | 0.087 | <0.001 | 0.0502 | 0.0882 | <0.001 |
| Mean | ND | <0.001 | <0.001 | <0.001 | <0.001 | 0.080 | <0.001 | 0.0308 | 0.0433 | <0.001 |
| Standard (OSHA : TWA) | 0.1 | 0.005 | 0.05 | 5 | 1 | 1 ppm | - | - | 100 ppm | 100 ppm |

3.3 Cancer risk and Non-cancer risk

VOCs concentrations were lower than time-weighted average (TWA) recommended by OSHA [12]. However lifetime cancer risk (leukemia) of being exposed to benzene by inhalation from working in feeding area, operation room, and office were 8.88 x 10-6, 1.53 x 10-5, and 1.38 x 10-5 respectively. (Table 2) The cancer risk was exceeding the acceptable of 1 in 1,000,000. While risk estimates of non-cancer effects not exceed the risk level (both HQ and HI were lower than 1).

Table 2 Cancer risk and non-cancer risk

|  | Cancer Risk | Non-Carcinogenic risk (Hazard Quotient : HQ) |
| --- | --- | --- |
|  | Benzene | Toluene | Ethylbenzene | Xylene | Styrene | Hazard Index : HI |
| Critical effect | Leukemia | Neurological effects | Developmenta toxicity | decreased rotarod performance | CNS effect |  |
|  | IUR: 7.8 x 10-6 per ug/m3 | RfC : 5 mg/m3 | RfC : 1 mg/m3 | RfC : 0.1 mg/m3 | RfC : 1 mg/m3 |  |
| Sampling Area |  |
| Feeding Area | 8.88 x 10-6 | 2.92 x 10-5 | 1.46 x 10-4 | 0.0015 | 1.46 x 10-4 | 0.002 |
| Operation Room | 1.53 x 10-5 | 2.92 x 10-5 | 1.22 x 10-2 | 0.12 | 1.46 x 10-4 | 0.132 |
| Office | 1.38 x 10-5 | 2.92 x 10-5 | 1.46 x 10-2 | 0.25 | 1.46 x 10-4 | 0.272 |
| Mean | 1.26 x 10-5 | 2.92 x 10-5 | 8.99 x 10-3 | 0.12 | 1.46 x 10-4 | 0.135 |

# Conclusion and Recommendation

Concentration of air heavy metal is quite not the problem in this study area and an average 8 hours of VOCs concentrations including benzene, toluene, ethylbenzene, xylene and styrene in this study lower than the occupational limit of that defined by international organization. However, benzene, ethylbenzene and xylene are consistently higher indoor (operation office and administrative office) than outdoor (fuel feeding area). In the same way lifetime cancer risk from benzene exposure via inhalation are higher indoor than out door. Some prevention measures should be taken to reduce risks, such as increasing of ventilation and using of air cleaners in indoor environment. In addition risk communication should be introduced to the staffs to protect themselves properly.

References

- Department of Pollution Control. 2014. A roadmap for waste and hazardous waste management. National Council for Peace and Order approved version. 26 August 2014.

- Gochfeld M. Incineration: health and environmental consequences. Mt Sinai J Med. 1995 Oct;62(5):365–374.

- Miyake Y, Yura A, Misaki H, Ikeda Y, Usui T, Iki M; Shimizu T. Relationship between distance of schools from the nearest municipal waste incineration plant and child health in Japan. European Journal of Epidemiology 2005; 20: 1023–1029.

- Shy, C.M., D. Degnan, D.L. Fox, S. Mukerjee, M.J. Hazucha, B.A. Boehlecke, D. Rothenbacher, P.M. Briggs, R.B. Devlin, D.D. Wallace, R.K. Stevens, and P.A. Bromberg. 1995. Do waste incinerators induce adverse respiratory effects? An air quality and epidemiological study of six communities. Environ. Health Perspect. 103(7-8):714-724.

- Maitre, A., Collot-Fertey, D., Anzivino, L., Marques, M., Hours, M., & Stoklov, M. (2003). Municipal waste incinerators: air and biological monitoring of workers for exposure to particles, metals, and organic compounds. Occupational and Environmental Medicine, 60(8), 563–569. http://doi.org/10.1136/oem.60.8.563

- U.S. Environmental Protection Agency [U.S, EPA]. Risk assessment guidance for superfund volume i: human health evaluation manual (Part F, Supplemental Guidance for Inhalation Risk Assessment). Washington, D.C: Office of Emergency and Re medial Response; 2009.

- U.S. Environmental Protection Agency, Integrated Risk Information System [IRIS]. Integrated risk information for benzene [Monograph on the internet]. Washington, DC: U.S. Environmental Protection Agency; 2003 [cited 2016 December 6]. Available from: https://cfpub.epa.gov/ncea/iris2/chemicalLanding.cfm?substance_nmbr=276

- U.S. Environmetal Protection Agency, Integrated Risk Information System [IRIS]. Integrated risk information for ehtylbenzene [Monograph on the internet]. Washington, DC: U.S. Environmental Protection Agency; 1991 [cited 2016 December 6]. Available from: https://cfpub.epa.gov/ncea/iris2/chemicalLanding.cfm?substance_nmbr=51

- U.S. Environmental Protection Agency, Integrated Risk Information System [IRIS]. Integrated risk information for toluene [Monograph on the internet]. Washington, DC: U.S. Environmental Protection Agency; 2005 [cited 2016 December 6]. Available from: https://cfpub.epa.gov/ncea/iris2/chemicalLanding.cfm?substance_nmbr=118

- U.S. Environmental Protection Agency, Integrated Risk Information System [IRIS]. Integrated risk information system for xylene [Monograph on the internet]. Washington, DC: U.S. Environmental Protection Agency; 2003 [cited 2016 December 6]. Available from: https://cfpub.epa.gov/ncea/iris2/chemicalLanding.cfm?substance_nmbr=270

- U.S. Environmental Protection Agency, Integrated Risk Information System [IRIS]. Integrated risk information system for Styrene [Monograph on the internet]. Washington, DC: U.S. Environmental Protection Agency; 1992 [cited 2016 December 6]. Available from: https://cfpub.epa.gov/ncea/iris2/chemicalLanding.cfm?substance_nmbr=104

- OSHA. (2012). Chemical sampling information. Retrieved April 21, 2014, from Occupational Safety & Health Administration [OSHA]: https://www.osha.gov/dts/chemicalsampling/toc/toc_chemsamp.html