# Overview of EIA systems in oil producing countries of Africa

# 1. Introduction

Within the last decade, African countries have discovered new oil deposits in commercial quantities (Aryeetey and Asmah 2011). The increase in countries with oil deposits has enhanced the importance of having effective Environmental Impact Assessment (EIA) systems and practice within the continent. EIA as a legal decision making tool, has existed since the enactment of the National Environmental Policy Act (1969) in the United States, and has since spread around the globe to nearly all countries (Morgan 2012). In most African countries, EIA was introduced in the early nineties due to pressure from international donors and in some cases; environmental disasters faced by countries within the continent (Kakonge 2006). This paper aims to evaluate and establish the legal framework for EIA systems in nineteen oil producing countries (See Figure 1) in Africa and propose recommendations for improvements. In doing so, the first section introduces the topic and the purpose of the research. The second section outlines the methodology while the third section summarizes the findings. Finally, conclusions are provided.

# Figure 1. Map of oil producing countries in Africa (source: author)

# 2. Methodology

The rationale for selecting the 19 countries was based on their location in Africa and their level of crude oil production (Minimum of 1000 barrels per day) (EIA 2014). The evaluation framework developed in this paper is adapted from Ahmad and Wood (2002). A total of 19 criterion are used which are grouped under three major headings- a) EIA legislation; EIA administration; EIA process (See Table 1).

Table 1. EIA evaluation criteria: systematic measures

(Source: adapted from Ahmad and Wood (2002)

Criteria

EIA legislation

1. Provisions for Environmental Impact Assessment

2. Year of enactment

3. Status of EIA regulation

4. Legal provision for appeal

5. Time limit

6. Strategic Environmental Assessment provision

EIA administration

7. Environmental Impact Association regulatory body

8. Review committee

9. Sectorial authority role

EIA practice

10. Screening

11. Scoping

12. Alternatives

13. EIA specified report content

14. Public participation in Environmental Impact Assessment

15. Environmental Management Plan required

16. Requirement for impact mitigation

17. Experience in Strategic Environmental Assessment

18. Sectorial authority regulation

19. EIA implementation monitoring

In evaluating the African countries against the criterion developed above, a systematic literature review was carried out.  Similar to an approach adopted by Jha-Thakur and Fischer (2016), this work reviews five leading journals on EIA including- a) Environmental Impact Assessment Review (EIA Review); b) Journal of Environmental Assessment Policy and Management (JEAPM); c) Impact Assessment and Project Appraisal Journal (IAPA); d) Journal of Environmental Planning Management (JEPM) and e) Journal of Environmental Management. This was further complemented by a wider literature review, documentary analysis (especially for French/Portuguese speaking countries) and input from EIA experts. Input from relevant environment ministry of the respective countries was sought. The summary of the findings is presented in Table 2.

# 3. Results and findings

Table 2 below shows the results of the review. Of the countries discussed in this paper, Algeria was the first to issue EIA legislation through the Law 83-03 of 1983 on the protection of the environment (CITET 2003). Followed by Congo (Brazzaville) in (1986) and Tunisia in (1988).

# Table 2. summary of the results of EIA legislation, administration and practice.

| Criteria | Summary |
| --- | --- |
| EIA legislation |  |
| 1. Provisions for Environmental Impact Assessment | In 17 countries |
| 2. Year of enactment | 1983 to 2011 |
| 3. Status of EIA regulation | 15 countries enacted and 2 drafted |
| 4. Legal provision for appeal | In 6 countries, not available in 8 countries and no information on 5 countries |
| 5. Time limit | In 5 countries with respect to submitting final report, specified time limits for components in 7 countries and no provision on 7 countries |
| 6. Strategic Environmental Assessment provision | SEA provision in 3 countries, and no provision on 16 countries |
| EIA administration |  |
| 7. Environmental Impact Association regulatory body | Multiple regulatory bodies in 7 countries, Single regulatory body in 10 countries and no information on 2 countries |
| 8. Review committee | In 14 countries, no provision in 1 country and no information on 4 countries |
| 9. Sectorial authority role | In 11 countries, no provision in 4 countries and no information on 4 countries |
| EIA practice |  |
| 10. Screening | In 15 countries, no provision in 1 country and no information on 3 countries |
| 11. Scoping | By proponent in 10 countries, by regulator in 4 countries and not specific on 5 |
| 12. Alternatives | Provision in 7 countries, no provision in 9 countries and no information on 3 |
| 13. EIA specified report content | Content specified in 15 countries, no specification in 2 countries and no information on 2 |
| 14. Public participation in Environmental Impact Assessment | Provision in 12 countries, no provision in 5 and no information on 2 |
| 15. Environmental Management Plan required | Provision in 11 countries, no provision in 6 countries and no information on 2 |
| 16. Requirement for impact mitigation | In 17 countries, no information in 2 |
| 17. Experience in Strategic Environmental Assessment | In 2 countries, no provision in 13 and no information on 4 |
| 18. Sectorial authority regulation | In 10 countries, no provision in 6 countries and no information on 3 countries |
| 19. EIA implementation monitoring | Legislated in 12 countries, no provision in 5 countries and no information on 2 |

There are three countries which seem to have the most matured EIA systems in Africa; Egypt, Ghana and South Africa relatively based on countries reviewed.

# EIA legislation

Majority of the EIA legislation were put in place from 1983 to 2000. Since then, there has been advancements within the scope of EIA and its aim to help achieve sustainable development. Most of the countries require review of the current EIA laws to bring it up to date with best practices. Appeal process is important especially as it provides an outlet for the aggrieved party to seek justice in a civilized manner. Most countries do not currently have legal provisions to appeal within their EIA legislation. To setup a comprehensive legal provision to appeal, it’s important to include an appeal procedure for all stakeholders (proponent, regulator and public) involved in the process. Also, considerations should be given in setting a time limit within which an appeal process should be concluded. SEA provisions are extremely lacking within the EIA legislations in oil producing countries in Africa. Currently SEA is in existence in sixty countries globally (Fundingsland Tetlow and Hanusch 2012) but only in three among the oil producing countries in Africa selected.

# EIA administration

Countries with multiple regulatory bodies need to ensure the EIA process is streamlined to reduce cost and bureaucracy. A common trend within countries with review committee’s is a non-technical person heading such committee. It is important to ensure committees have the needed technical capacities to make decisions on EIA applications. Sectoral authorities having a role is common in the countries reviewed. It is important to ensure there is no conflict of interest during the EIA process.

# EIA process

The scoping component of the EIA practice in most of the countries reviewed needs to be strengthened; this can be achieved by building the capacity of the EIA administrative staff in setting the terms of reference for the proponent or in verifying the scoping report submitted by the proponent. Lessons can be learned from the South African system; it is successful in finding realistic means to mitigate negative impacts and better technology to evaluate impacts on environment (Duthie 2001). Public stakeholders with vested interest should also be provided an opportunity to participate at the scoping stage of the project, as their local knowledge of the study area cannot be overemphasized. Environmental Management Plan (EMP) and the implementation of monitoring are essential components within practice for an approved EIA to be a success. These components ensure the purpose of an EIA is not defeated. Setting a management plan with targets is of utmost necessity to ensure implementation and monitoring of mitigation measures contained in an EIA. The monitoring of projects also needs to be more thorough and frequent and monitoring reports needs to be made available to the public.

# 4. Conclusion

The trends recognized by this paper suggests that the EIA approach of most African oil producing countries is still at the foundation stage of managing negative environmental impacts. The decision-making process is still opaque and EIA’s ability to encourage sustainable development is not being utilized. Sustainable development can be enhanced, by opening the EIA process to public scrutiny and engaging more with community member of communities where projects are being situated.

# 5. References

Ahmad, B and Wood, C (2002), 'A comparative evaluation of the EIA systems in Egypt, Turkey and Tunisia', Environmental Impact Assessment Review, 22 (3), 213-34.

Aryeetey, E and Asmah, E (2011), Africa’s New Oil Economies: Managing Expectations (Washington, DC.: Brookings Institution).

CITET (2003), 'Working together to strengthen the environment', strengthening EIA systems in the Mediterranean region.

Colón, M. C and Gerena, E. T (2014), 'Oil and gas regulation in Equatorial Guinea: overview', in Practical Law (ed.), MULTI-JURISDICTIONAL GUIDE 2014

ENERGY AND NATURAL RESOURCES (Thomson Reuters).

Congo, Republic of the (2009), 'Décret N86/775 du 7/06/86 Rendant obligatoires les Etudes d'Impact

sur l'Environnement ', in MINlSTERE DU DEVELOPPEMENT DURABLE. DE L'ECONOMIE FORESTIERE and ET DE L'ENVIRONNEMENT. (eds.).

Dieudonne, A. (2007), 'The oil industry along the Atlantic coast of Cameroon: Assessing impacts and possible solutions', Resources Policy, 32 (3), 135-45.

DRC 'Environmental and Social Management Framework', <http://documents.worldbank.org/curated/en/889041467996698593/text/E4838-V1-EA-P124072-Box396263B-PUBLIC-Disclosed-5-27-2016.txt>, accessed.

Duthie, A. G. (2001), 'A review of provincial environmental impact assessment administrative capacity in South Africa', Impact Assessment and Project Appraisal, 19 (3), 215-22.

EIA 'Total petroleum and other liquids production', <http://www.eia.gov/beta/international/data/browser/index.cfm - /?pa=0000000000000000000000000000000000vg&c=ruvvvvvfvtvvvv1vvvvvvfvvvvvvfvvvsu20evvvvvvvvvvvfuvg&ct=0&tl_id=5-A&vs=INTL.53-1-AFG-TBPD.A&ord=SA&vo=0&v=C&start=1980&end=2014&vid=1>, accessed 13th February 2017.

El-Zayat, H., Ibraheem, G., and Kandil, S. (2006), 'The response of industry to environmental regulations in Alexandria, Egypt', Journal of Environmental Management, 79 (2), 207-14.

Fundingsland Tetlow, Monica and Hanusch, Marie (2012), 'Strategic environmental assessment: the state of the art', Impact Assessment and Project Appraisal, 30 (1), 15-24.

Guinea, Republic of Equatorial (2006a), 'HYDROCARBONS LAW OF THE REPUBLIC OF EQUATORIAL GUINEA', in presidency (ed.), (8; Equitorial Guinea).

--- (2006b), 'MINING LAW FOR THE REPUBLIC OF EQUATORIAL GUINEA Law 9/2006', in presidency (ed.), (9; Equitorial Guinea).

--- (2006c), 'PETROLEUM REGULATIONS OF THE REPUBLIC OF EQUATORIAL GUINEA', presidency, Equitorial Guinea.

Jha-Thakur, U. and Fischer, Thomas B. (2016), '25 years of the UK EIA System: Strengths, weaknesses, opportunities and threats', Environmental Impact Assessment Review, 61, 19-26.

Kakonge, J. O. (2006), 'Environmental Planning in Sub-Saharan Africa: Environmental Impact Assessment at the Crossroads', Working Paper 9.

Mbile, P., et al. (2005), 'Linking management and livelihood in environmental conservation: case of the Korup National Park Cameroon', Journal of Environmental Management, 76 (1), 1-13.

Morgan, Richard K. (2012), 'Environmental impact assessment: the state of the art', Impact Assessment and Project Appraisal, 30 (1), 5-14.

Zhang, Jie, Kørnøv, Lone, and Christensen, Per (2013), 'Critical factors for EIA implementation: Literature review and research options', Journal of Environmental Management, 114, 148-57.