Water quality and Health Risk Assessment on Arsenic and Manganese Exposure of Community Located in the Border Adjoining Phichit, Phetchabun and Phitsanulok Provinces, Thailand

Abstract

This cross-sectional study research aimed to determine water consumption sources, assess the risk on manganese and arsenic exposure due to consumption of well water and village water supply in community located in the border adjoining Phichit, Phetchabun and Phitsanulok Provinces in Thailand. The interviews of 314 households on the water consumption behavior were conducted. The water from 18 wells and 49 village water supply were analyzed for difference quality parameters.   The studied found that there were approximately  5% and 6% of households that using well water for cooking, and using water supply for drinking purpose respectively. The concentration of heavy metal namely Cr,Cd,As,Hg   in water-well were not found while As were found  below the drinking water standard in village tap water samples. The concentration of manganese in well water and village water supplies varied from 0.002 to 2.64 mg/l and from 0.002 to 1.12 mg/l respectively. Health risk assessment of manganese and arsenic exposure was performed at an intake rate of the water samples (at 97.5 percentile). Health risk associated with manganese exposure was at acceptable level. In addition, the average skin cancer risk in age group of 3 years and over due to consuming tap water for drinking purpose were not exceed the acceptable of 1 in 1,000,000.However the maintenance of village water supply system is recommended.

1. Introduction

Metal are high conductivity substance and occur naturally in the earth’s crust which vary composition among difference areas. Metals in water supply may occur naturally or may be the result of contamination such as arsenic, cadmium, chromium, manganese, and mercury. Inorganic arsenic is highly human toxic while organic compound are less toxic to human health. Inorganic arsenic exposure in drinking water is known to course skin cancer and it has been associated with adverse reproductive outcomes (ATSDR, 2007; Kim Yoon-J; Smith et.al., 1992). Manganese is a grey white metal and it is an essential nutrient. Several enzyme catalytic system and cell function depend on manganese.  The formulation of cartilage and bone require manganese. In addition manganese is required for the maintenance of mitochondria and the production of glucose. Epidemiological studies both in children and elderly have found that extremely high levels of manganese exposure may lead to neurological and brain development effects (ATSDR, 2012; U.S.EPA, 2004).

According to the Thailand drinking water surveillance report, it was found that manganese level in the village water supply exceeded the drinking water standard in the adjoined area of Phichit, Phetchaboon and Phitsanuloke provinces which located at the gold belt area.  In addition, there is a gold mining operation in a short distance from the village which manganese and arsenic contamination in the monitoring wells were exceeded surface water standard at many stations.The objective of this study are to determine water consumption sources, and to determine health risk from arsenic and manganese exposure in well and tap water in community located in the border adjoining Phichit, Phetchabun and Phitsanulok Provinces,Thailand.

2. Material and methods

2.1 Source of drinking water determination

An interview was conducted to collect community source of drinking water. A structure of questionnaire included detailed questions on drinking and cooking source. This study focused on 24 villages of the three adjoining provinces in  northern  part of Thailand namely Phichit, Phetchaboon and Phitsanuloke. Ten percent of total household in 24 villages were random selected which was 400 out of 3,981 household.

2.2 Sampling and analytical of heavy metals in drinking water

A hundred percent of village water supply and well water that used for drinking purpose across 24 villages were selected. The sample was collect twice in March and September 2016.The water samples from  49 tap water stations and 67 wells were collected. Heavy metals concentrations namely arsenic, cadmium, chromium, manganese, and mercury were analyzed following the Standard Method for the examination of water and wastewater (APHA,AWWA,WEF, 2012).

2.3 Health risk assessment

In this process, information is analyzed to determine if hazards might cause adverse effects following exposure to a risk source. Manganese and arsenic exposure assessment and risk characterization were assessed by following the United States Environmental Protection Agency guidance (U.S.EPA.1989a, 2001).The most common measure are the chronic daily intake (CDI). Risk characterization of noncancer effects due to manganese and arsenic exposure were then evaluated by comparing an exposure level (CDI) with toxicity value (RfC) which expressed in term of hazard quotient (HQ). If the calculated HQ is equal or less than 1, noncancer adverse effects due to drinking water pathway is assumed to be negligible.   For the risk estimated of an individual developing cancer over a life time due to inorganic arsenic exposure is expressed as cancer risk (CR) which accepted in the range of 1x10-4 to 1x10-6.

Drinking water exposure and risk equations that used in risk calculations, in this study, were calculated as follows:

Exposure assessment:               (1)

Cancer risk assessment:                 (2)

Noncancer risk assessment:                     (3)

Where: CDI is chronic daily intake of arsenic and manganese (mg/kg-day); C is the concentration of inorganic arsenic and manganese in tap water and well water (mg/L).; IR is the ingestion rate (L/day); EF is the exposure frequency (days/year);ED is the exposure duration (years);BW is the body weight (Kg); AT is the averaging time, (equal to ED x 365 days/year for noncarcinogen and 70 years x 365 day/years for carcinogen); CSF is the cancer slope factor for inorganic arsenic (mg/kg-day)-1; RfC is the reference concentration for the manganese and inorganic arsenic for assessing noncancer health effects (mg/kg-day). Total arsenic concentration in water samples was assumed to be inorganic arsenic and 100% absorption. In the same manner, manganese concentration in water samples was assumed 100% absorption.

Arsenic and manganese exposure and risk characterization for eight different age groups were calculated including 0 to 3 year, 3 to 6 year,6 to 9 year,9 to16 year, 16 to 19 year, 19 to 35 year, 35 to 65 year and >65 year. Exposure parameter were used from National study of food consumption data which was study by National Bureau of Agricultural Commodity and Food Standards (ACFS, 2006), Thailand.

Health risk was determined under the worst scenario of exposure where 97.5th percentile of drinking water consumption in different age groups and 97.5 th percentile of manganese and arsenic concentration were used.

3. Results

3.1 The community source of drinking water

Three hundred and fourteen randomly selected household were successfully interviewed (7.8 percent of total household). This study found that most of the household in the community has been used bottled water, rain water and tap water for drinking purpose at approximately 65%, 14% and 6 % respectively. In the same time, bottled water, tap water, rain water, and well water has been used for cooking purpose at approximately 39%, 29%, 11%,and 5.1% respectively as showed in table 1.

Table 1 Source of drinking water in the community

| Source of Drinking Water | Number (Percentage) |
| --- | --- |
|  | Bottled Water | Rain Water | Bottled and Rain Water | Tap water | Tap and Bottled Water | Well | Tap and Rain Water | Others |
| Drinking | 205 (65.3) | 43 (13.7) | 26 (8.3) | 19 (6.1) | 0 | 0 | 0 | 21 (6.7) |
| Cooking | 123 (39) | 35 (11) | 6 (1.9) | 90 (29) | 23 (7.3) | 16 (5.1) | 15 (4.8) | 6 (1.9) |

  - Heavy metal concentrations

The sample from forty nine tap water stations and 67 wells were collected and analyzed manganese, chromium, cadmium, arsenic, and mercury concentrations in March and September 2016. The concentrations of chromium, cadmium, and mercury were not found in both tap and well water. The mean, minimum, maximum, and 97.5th percentile of manganese and arsenic were evaluated and showed in table 2.

Table 2   Metals concentration in drinking water

| Metals | Tap Water | Well Water |
| --- | --- | --- |
|  | Mean (mg/L) | Min-Max (mg/L) | 97.5th percentile | Mean (mg/L) | Min-Max (mg/L) | 97.5th percentile |
| Manganese | 0.16 | 0.0015-1.124 | 0.973 | 0.43 | 0.002-2.64 | 2.30 |
| Chromium | ND | ND | - | ND | ND | - |
| Cadmium | ND | ND | - | ND | ND | - |
| Arsenic | 0.006 | 0.005-0.007 | 0.007 | ND | ND | - |
| Mercury | ND | ND | - | ND | ND | - |

  - Exposure and Health Risk Evaluation

The 97.5th percentile of manganese and arsenic concentration, 0.973 and 2.3 mg/L, were used to estimate risk. This study assumed total arsenic concentration analyzed as inorganic arsenic form. The amount of intake rate were 97.5th percentile of national intake rate, range from 0.78-2.1 liters per day, and rely up on eight difference age groups. In addition, exposure duration and body weight were range from 3 to 31 years and 10-60 kilograms respectively. Exposure parameters used in this study were showed in Table 3.

Table 3 Exposure parameter used in risk analysis

| Variables | Values | Units | References |
| --- | --- | --- | --- |
| Concentration of Mn in tap water | 0.973 | mg/L | This study |
| Concentration of Mn in well water | 2.3 | mg/L | This study |
| Concentration of Inorganic As in tap water | 0.007 | mg/L | This study |
| IR | 0to3year =0.781 3to6year =1.1 6to9year =1.2 9to16year =1.6 16to19year =1.8 19to35year =2.05 35to65year =2.1 >65 year =1.9 | L/day | ACFS,2006 |
| EF | 365 | day/year | (U.S.EPA.1989a, 2001) |
| ED | 0to3year = 3 3 to 6year =3 6to9year = 3 9 to16year =7 16to19year = 3 19 to35year =16 35to60year = 31 >65 year =5 | year | Constance |
| BW | 0to3year =10 3to6year =17.1 6to9year =22.8 9to16year =39.73 16to19 year =53.23 19to35year =58.28 35 to 65 year =60.37 >65 year =54.53 | kg | (ACFS, 2006) |
| AT | EDx365 | year | (U.S.EPA.1989a, 2001) |
| RfC (Mn) | 0.14 | mg/kg-day | (U.S.EPA.IRIS, 1988) |
| RfC (Inorganic As) | 0.0003 | mg/kg-day | (U.S.EPA.IRIS, 1988) |
| CSF (Inorganic As) | 5x10-8 | unitless | (U.S.EPA.IRIS, 1988) |

3.3.1) Noncancer risk

The CDI and risk characterization of manganese and arsenic via drinking water in different age groups were demonstrated in table 4 and 5. Risk characterization of noncancer effects from exposure to manganese and arsenic in tap water and well water in term of HQ were lower than 1, indicated that adverse effects due to manganese and arsenic exposure is assumed to be acceptable.

Table 4 The outputs of manganese exposure assessment and risk characterization

| Results | Non-cancer effects |
| --- | --- |
|  | Tap water | Well water |
| Age group | CDI (mg/kg-day) | HQ | CDI (mg/kg-day) | HQ |
| 0-3 | 0.0032 | 0.02 | 0.0076 | 0.05 |
| 3-6 | 0.0027 | 0.02 | 0.0063 | 0.05 |
| 6-9 | 0.0022 | 0.02 | 0.0052 | 0.04 |
| 9-16 | 0.0039 | 0.03 | 0.0093 | 0.07 |
| 16-19 | 0.0014 | 0.01 | 0.0033 | 0.02 |
| 19-35 | 0.0078 | 0.06 | 0.0185 | 0.13 |
| 35-65 | 0.0145 | 0.10 | 0.0343 | 0.24 |
| >65 | 0.0024 | 0.02 | 0.0057 | 0.04 |

3.3.2) Cancer risk

The increased cancer risk of being exposed to inorganic arsenic by water consumption in different age groups were 5.1 x10-13 to 5.2 10-12   as showed in table 5. The cancer risk was not exceed the acceptable of 1 in 1,000,000. In conclusion, risk estimates of both noncancer and cancer effects not exceed the risk level.

Table  5 The outputs of arsenic in tap water exposure assessment and risk characterization

| Age group | Non-cancer effects | Cancer effects |
| --- | --- | --- |
|  | CDI (mg/kg/day) | HQ | CDI (mg/kg/day) | CR |
| 0-3 | 0.000023 | 0.08 | 0.000023 | 1.1x10-12 |
| 3-6 | 0.000019 | 0.06 | 0.000019 | 9.7 x10-13 |
| 6-9 | 0.000016 | 0.05 | 0.000016 | 7.9 x10-13 |
| 9-16 | 0.000028 | 0.09 | 0.000028 | 1.4 x10-12 |
| 16-19 | 0.000010 | 0.03 | 0.000010 | 5.1 x10-13 |
| 19-35 | 0.000056 | 0.19 | 0.000056 | 2.8 x10-12 |
| 35-65 | 0.000104 | 0.35 | 0.000104 | 5.2 x10-12 |
| >65 | 0.000017 | 0.06 | 0.000017 | 8.7 x10-13 |

4. Discussion

Among the fourth classified sources, bottled water, rain, and tap constitute a major proportion of main source of drinking water in this area which relatively same as Thailand’s source of drinking water (Thaihealth, 2015). Manganese and arsenic concentration may differ between raw water and treated water as well as the depth of water well. The effective village bottled water production as well as water supply treatment should be maintained for sustain drinking water quality. Water and foods are major potential sources of arsenic exposure. Hence ,more research is needed to assess the variation of inorganic arsenic and manganese in different types of food in this area.

6. References

ACFS. (2006). Food consumption data of Thailand. Thailand: The national bureau of agricultural commodity and food standards(ACFS).

APHA,AWWA,WEF. (2012). Standard methods for the examination of water and wastewater (22nd edition). Washington: American Public Health Association.

ATSDR. (2007). Toxicological profile for arsenic. Department of Health and Human Serveices.United States of America.Retrieved 12,2016,from http://www.atsdr.cdc.gov/

toxprofiles/tp2.html.

ATSDR. (2012). Toxicological profile for manganese. Department of Health and Human Serveices.United States of America.Retrieved 12,2016,from http://www.atsdr.cdc.gov/

toxprofiles/tp2.html.

Department of Health. (2014). Drinking water monitoring report. Thailand.

Kim Yoon-Jae, K. J.-M. (2015). Arsenic toxicity in maale reproduction and development. Dev.Reprod., 19:167-180.

Monisha Jaishankar, T. T. (2014). Toxicity, mechanism and health effects of some heavy metals. Interdiscip Toxical., 60-72.

P.D. Howe, H. M. (2004). Manganese and its compounds:Enivronmental aspects. Geneva: World Health Organization.

Smith et.al., A. H. (1992). Cancer risks from aresnic in drinking water. Environmental Health Perspectives, 97:259-267.

Thaihealth. (2015). Health news:Thailand' patients drinking water per year over one million people. Retrieved February 11, 2017, from Thai Health Promotion Foundation: www.thaihealth.or.th

U.S.EPA. (2004). Drinking water health advisory for manganese. Washington,DC.

U.S.EPA.1989a. (2001). Risk assessment guidance for superfund:Volume III-PartA,Process for conducting probabilistic risk assessment. Washington.

U.S.EPA.IRIS. (1988, 10 2). IRIS summary of inorganaic arsenic. Retrieved November 2016, from Integrate Risk Information System: https://cfpub.epa.gov/ncea/iris/iris_documents/documents/subst/0278_summary.pdf

U.S.EPA.IRIS. (1988, 9 26). Summary document of manganese. Retrieved 11 2016, from Integrate Risk Information System: https://cfpub.epa.gov/ncea/iris/iris_documents/documents/subst/0373_summary.pdf